## Slide 1: ECEN 404: Active Ankle- Foot Orthosis (AAFO)
Alfred Boss
Christopher Galik
Tyler Pierce

## Slide 2: System Overview
EMG sensors and FSR sensors will measure electrical activity and pressure in the leg and foot.
The AAFO will transport signals from the 2 sensors to the MCU.
The microcontroller will interpret signals and determine which stage of gait the user is in and supply corresponding motor control.
The motion system, which acts as an artificial muscle, will move the joint by attaching to a rigid structure.

## Slide 3: Sensor & MicroController System
Last Semester Accomplishments
Identified proper locations for two FSR sensors (ball & heel) and 1 EMG sensor (soleus)
Simulated, Designed, and Built circuits to run the sensors
Tested and tweaked all sensors to acquire proper results for all tests
Wrote code for arduino to show sensors function on the system’s microcontroller
Successfully demonstrated all sensors show expected results on the Arduino Uno Rev3
Ongoing progress/problems
Need to understand Polina’s code and confirm it functions properly.
If code does not function properly, then it will need to be tweaked and commented
Need to integrate code with sensors

## Slide 4: Artificial Muscle/Motion System Development
Updates
  Part replacement for stronger baseline strength
Upcoming
  Do power test to ensure smooth integration into the power system
  Prep artificial muscle component for integration into the structure

## Slide 5: Structural Design
Updates
  Dual Artificial Muscle design
  Finalized 1st iteration structure design with sponsor
  Axis Hinge
Upcoming
  Double check measurements
  Start 3D printing components today/tomorrow
  Validate with stress testing on optical treadmill
  Design changes as needed

## Slide 6: Power System
Updates
  Current design is 2 Amps max
  Dual Artificial Muscle has doubled power requirements (4 Amps+)
  Pad separating ground plane came off during PCB soldering
Upcoming
  Research new design for new power requirements
  “Ground up” and pre-built options
Notes: 10 pins power req for MC, 0.7A for max current needed for AM, 0.65 minimum, switch solution for speed control

## Slide 7: Execution Plan